DRAFT

SKS (Secure Key Store)
TEE/SE Mapping

Disclaimer: This is a system in development. That is, the specification may change without notice.

# Introduction
This document describes a possible way to map a TEE (Trusted Execution Environment) and an SE (Security Element) in order to emulate an SKS (Secure Key Store).
The assumption is that the SE has limited storage capability. In fact, in this specification the SE doesn't have to have any persistent storage, only RAM for executing cryptographic operations. The SE may be a specific component or it may be a part of an enhanced TPM (Trusted Platform Module). An SE could also be implemented using schemes like ARM's TrustZoneTM.
The TEE is assumed to be trustworthy which in this design includes the ability to perform all access control needed for using and managing credentials based on cryptographic keys. How the TEE is secured is out-of-scope for this but it can involve anything from process running a kernel level to operating systems secured by TPMs.
Note: this is by no means the only way of partitioning the work between a TEE and an SE!

# Architecture
Below is a picture showing the core components in the SKS architecture:
The Device Certificate forms together with a matching Attestation Private Key the foundation for the session mechanism that facilitates secure provisioning of keys, also when the provisioning middleware and network are non-secure.
The Credential Database holds keys and other data that is related to keys such as protection and extension objects. It also keeps the provisioning state.
The Cryptographic Engine performs in addition to standard cryptographic operations on private and secret keys, the core of the provisioning operations which from an API point-of-view are considerably more complex than the former.
A vital part of the Cryptographic Engine is a high quality random number generator since the integrity of the entire provisioning scheme is relying on this.
All operations inside of an SKS are supposed to be protected from tampering by malicious external entities but the degree of internal protection may vary depending on the environment that the SKS is running in. That is, an SKS housed in a smart card which may be inserted in an arbitrary computer must keep all data within its protected memory, while an SKS that is an integral part of a mobile phone processor may store credential data in the same external Flash memory where programs are stored, but sealed by a CPU‑resident “Master Key”.

# Provisioning API
Although SKS may be regarded as a “component”, it actually comprises of three associated pieces: The KeyGen2 protocol, the SKS architecture, and the provisioning API described in this document. These items are tightly matched to form the foundation for secure and interoperable ecosystems for provisioning and managing cryptographic keys.
One of the core features of the SKS Provisioning API is enabling independent issuers to securely share a single “Key Ring”. The rationale for this is mainly to support mobile phones with embedded “Trusted Hardware”, but it appears that the already quite popular USB memory sticks augmented with SKS functionality would be a realistic product offering if they could deal with a potentially large chunk of a consumer's authentication hassles on the Internet.
## Backward Compatibility
A question that arises is of course how compatible the SKS Provisioning API is with respect to existing protocols, APIs, and smart cards. The answer is simply: NOT AT ALL due to the fact that current schemes do generally not support secure on-line provisioning and key life-cycle management directly towards end-users.
In fact, smart cards are almost exclusively personalized by more or less proprietary software under the supervision of card administrators or performed in automated production facilities. It is evident that (at least) mobile phones need a scheme that is more consistent with the on-line paradigm since SIM-cards due to operator-bindings do not scale particularly well.
“On the Internet anybody can be an operator of something”
Although the lack of compatibility with the current state-of-the-art (“nothing”), may be regarded as a major short-coming, the good news is that SKS by separating key provisioning from actual usage, does neither require applications nor cryptographic APIs to be rewritten. See next section.
# User API
In this document “User API” refers to operations that are required by security applications like TLS client-certificate authentication, S/MIME, and Kerberos (PKINIT).
The User API is not a core SKS facility but its implementation is anyway recommended, particularly for SKSes that are featured in “connected” containers such as smart cards since smart card middleware has proved to be a major stumbling block for wide-spread adoption of PKI cards for consumers.
The described User API is fully mappable to the subset of CryptoAPI, PKCS #11, and JCE that the majority of current PKI‑using applications rely on.
The standard User API does not utilize authenticated sessions like featured in TPM 1.2 because this is a local security option, which is independent of the network centric Provisioning API.
If another User API is used the only requirement is that the key objects created by the provisioning API, are compatible with the former.

# Security Model
Since the primary target for SKS is authentication to arbitrary service providers on the Internet, the security model is quite different to traditional multi-application card schemes like Global Platform. In practical terms this means that it is the user who grants an issuer the right to create keys in the SKS. That is, there are no preconfigured “Security Domains”.
However, an issuer may during a provisioning session define a VSD (Virtual Security Domain) which enables post provisioning (update) operations by the issuer, while cryptographically shielding provisioned data from similar actions by other issuers.
When using KeyGen2 the grant operation is performed through a GUI dialog triggered by an issuer request, which in turn is the result of the user browsing to an issuer-related web address.
The SKS itself only trusts inbound data that can securely be derived from a session key created in the initial phase of a provisioning session. See createProvisioningSession.
The session key scheme is conceptually similar to Global Platform's SCP (Secure Channel Protocol) but details differ because KeyGen2 uses an on-the-wire XML format requiring encoding/decoding by the middleware, rather than raw APDUs.
Regarding who trusts an SKS, this is effectively up to each issuer to decide and may be established anytime during an enrollment procedure. Trust in an SKS can be highly granular like only accepting requests from preregistered units or be fully open ended where any SKS complaint device is accepted. A potentially useful issuer policy would be specifying a set of endorsed SKS brands, presumably meeting some generally recognized certification level like EAL5.
Many smart card schemes depend on roles like SO (Security Officer) which squarely matches scenarios where users are associated with a multitude of independent service providers. By building on an E2ES (End To End Security) model, the technical part of the SO role, exclusively becomes an affair between the SKS and the remote issuers, where each issuer is confined to their own virtual cards and SO policies.
Also see Security Considerations.
# Transaction Based Operation
An important characteristic for maintaining integrity and robustness is that provisioning and management operations either succeed or leave the system intact. This is in SKS accomplished by deferring the actual execution of container-modifying operations until the terminating closeProvisioningSession call.
Ideally an SKS container should be able dealing with power-failures regardless when they occur.

# Objects
The SKS API (as well as its companion protocol KeyGen2), assumes that objects are arranged in a specific fashion in order to work. At the heart of the system there are the typical cryptographic keys intended for user authentication, signing etc., but also dedicated keys supporting life-cycle management and of user keys and attributes.
All provisioned user keys, including symmetric dittos (see setSymmetricKey), are identified by X.509 certificates. The reason for this somewhat unusual arrangement is that this enables universal key IDs as well as secure remote object management by independent issuers. See Remote Key Lookup.
Note: unlike 7816-compatible smart cards, an SKS exposes no visible file system, only objects.

## Key Entries
The following picture shows the components forming an SKS key entry:
Public Key denotes the public part of the key-pair created by createKeyPair.
Private Key denotes the private part of the key-pair created by createKeyPair.
End‑Entity Certificate denotes the X.509 certificate set by the mandatory call to setCertificatePath.
Secret Key denotes an optional secret key defined by calling setSymmetricKey.
CA Certificates denote optional X.509 CA certificates defined during the call to setCertificatePath.
Extension Objects denote optional extension objects defined by calling addExtension.
PIN Error Count denotes a counter associated by keys protected by a PIN policy object. See createPINPolicy.
Key Attributes denote the attributes defined during the call to createKeyPair.
Note that the key management methods always involve an entire key entry; individual components cannot be managed.
## Key Protection Objects
Keys can optionally be protected by PIN-codes (“passphrases”). PIN-protected keys maintain separate PIN error counters, but a single PIN policy object may govern multiple keys. A PIN policy and its associated keys can in turn be supplemented by an optional PUK (PIN Unlock Key) policy object that can be used to reset error-counters that have passed the limit as defined by the PIN policy. Below is an illustration of the SKS protection object hierarchy:

For the creation of protection objects, see createPUKPolicy, createPINPolicy and createKeyPair.
For an example how KeyGen2 deals with this structure, see KeyInitializationRequest.
Note that the set of keys bound to a particular PIN policy object “owns” the PIN policy object which means that when the last key of such a set has been deleted, the PIN policy object itself must be automatically deleted (by pp_deleteKey and deleteKey). The very same principle is also valid for PUK policy objects. Due to this there are no specific PIN or PUK delete methods.
An SKS may also support a device (system-wide) PIN and PUK. See getDeviceInfo. Management of device PINs and PUKs is out of scope for the SKS API.

## Provisioning Objects
The following picture shows how provisioning objects “own” the keys they have provisioned:

For detailed information concerning the contents of a provisioning object see createProvisioningSession.
Note that when the last key owned by a provisioning object has been deleted, the provisioning object itself must be automatically deleted (by closeProvisioningSession and deleteKey).
If a KeyManagementKey is deployed during provisioning object creation (establishing a VSD), post-provisioning operations can also be performed. See pp_deleteKey, pp_unlockKey, pp_updateKey, and pp_cloneKeyProtection.
# Algorithm Support
Algorithm support in SKS must as a minimum include the following items:
URI	Comment

Symmetric Key Encryption
http://www.w3.org/2001/04/xmlenc#aes128-cbc	See XML Encryption. Note that IV must be internally generated as well as prepended to encrypted data
http://www.w3.org/2001/04/xmlenc#aes192-cbc
http://www.w3.org/2001/04/xmlenc#aes256-cbc
http://xmlns.webpki.org/keygen2/1.0#algorithm.aes.cbc.pkcs5	See FIPS 197. Support for 128, 192, and 256-bit keys
http://xmlns.webpki.org/keygen2/1.0#algorithm.aes.ecb.nopad

HMAC Operations
http://www.w3.org/2000/09/xmldsig#hmac-sha1	See HMAC-SHA1
http://www.w3.org/2001/04/xmldsig-more#hmac-sha256	See HMAC-SHA256

Asymmetric Key Encryption
http://www.w3.org/2001/04/xmlenc#rsa-1_5	See XML Encryption	Decryption mode only
http://xmlns.webpki.org/keygen2/1.0#algorithm.rsa.raw	Non-padded RSA operation

Diffie-Hellman Key Agreement
http://xmlns.webpki.org/keygen2/1.0#algorithm.ecdh	See SP800-56A ECC CDH primitive (Section 5.7.1.2)

Asymmetric Key Signatures
http://www.w3.org/2000/09/xmldsig#rsa-sha1	See XML Signature	Signing mode only
http://www.w3.org/2001/04/xmldsig-more#rsa-sha256
http://www.w3.org/2001/04/xmldsig-more#ecdsa-sha256
http://xmlns.webpki.org/keygen2/1.0#algorithm.rsa.none	See signHashedData
http://xmlns.webpki.org/keygen2/1.0#algorithm.ecdsa.none

Elliptic Curves
urn:oid:1.2.840.10045.3.1.7	Also known as “P-256”. See FIPS 186-3

Special Algorithms
http://xmlns.webpki.org/keygen2/1.0#algorithm.sks.s1	See createProvisioningSession
http://xmlns.webpki.org/keygen2/1.0#algorithm.sks.k1	See createKeyPair
http://xmlns.webpki.org/keygen2/1.0#algorithm.none	See createKeyPair and setSymmetricKey

Supported algorithms can be acquired by calling getDeviceInfo which also lists RSA key generation capabilities which must include 1024 and 2048 bit keys.
# Key Protection Attributes
The following section describes the attributes issuers need to set for defining suitable key protection policies. Also see getKeyProtectionInfo, PrivateKeyBackup, KeyManagementKey, DevicePINProtection, and EnablePINCaching.
During provisioning of user defined PINs, the provisioning middleware should maintain the PIN policy and optionally ask the user to create another PIN if there is a policy mismatch because createKeyPair must return an error and abort the entire session if fed with incorrect data.
In addition to protection policies, a key may also be constrained with respect to algorithm usage. See EndorsedAlgorithms.

## Key Export
The following table illustrates the use of the ExportProtection attribute:
KeyGen2 Name	Value	Comment
none	0x00	No authorization needed for exporting the key
pin	0x01	Correct PIN is required
puk	0x02	Correct PUK is required
non-exportable	0x03	The key must not be exported

Also see exportKey.

## Key Delete
The following table illustrates the use of the DeleteProtection attribute:

KeyGen2 Name	Value	Comment
none	0x00	No delete restrictions apply
pin	0x01	Correct PIN is required
puk	0x02	Correct PUK is required
non-deletable	0x03	The key must not be deleted

Also see deleteKey.

## PIN Input Methods
The InputMethod policy attribute tells how PINs should be inputted to the SKS according to the following table:
KeyGen2 Name	Value	Comment
programmatic	0x01	PINs should only be given through the SKS User API
trusted-gui	0x02	Keys should only be used through a trusted GUI that does the actual PIN request and API invocation
any	0x03	No restrictions

Note that this policy attribute requires that the middleware is “cooperative” to be enforced.

## PIN Patterns
The PatternRestrictions policy attribute specifies how PINs must be designed according to the following table:
KeyGen2 Name	Value	Comment
two-in-a-row	0x01	Flags 1124 as invalid
three-in-a-row	0x02	Flags 1114 as invalid
sequence	0x04	Flags 1234, 9876, etc as invalid
repeated	0x08	All PIN bytes must be unique
missing-group	0x10	The PIN format must be alphanumeric or string and contain a mix of letters and digits. The string format also requires lowercase letters and non-alphanumeric characters. See PIN and PUK Formats

Note that the PatternRestrictions byte actually holds a set of bits. That is, 0x00 means that there are no pattern restrictions, while 0x06 imposes two constraints. Also note that pattern policy checking is supposed to be applied at the binary level which has implications for the binary PIN format (see PIN and PUK Formats).
For organizations having very strict or unusual requirements on PIN patterns, it is recommended letting the user define PINs during enrollment in a web application and then deploy issuer-set PIN codes during provisioning.

## PIN and PUK Formats
PINs and PUKs must adhere to one of formats described in the following table:
KeyGen2 Name	Value	Comment
numeric	0x00	0 - 9
alphanumeric	0x01	0 - 9, A - Z
string	0x02	Any valid UTF-8 string
binary	0x03	Binary value, typically issued as hexadecimal data

Note that format specifiers only deal with how PINs and PUKs are treated in GUIs; internally and in the SKS API, key protection data must always be handled as decoded strings of bytes. A conforming SKS must perform syntax validation during createKeyPair on numeric and alphanumeric PIN data. Length of the clear-text binary value must not exceed 128 bytes. See Format attribute in createPINPolicy and createPUKPolicy.

## PIN Grouping
A PIN policy object may govern multiple keys. The Grouping policy attribute (which is intimately linked to the Key Application Usage scheme), controls how PINs to the different keys relate to each other according to the following table:
KeyGen2 Name	Value	Comment
none	0x00	No restrictions
shared	0x01	All keys share the same PIN (synchronized)
signature+standard	0x02	Keys with AppUsage = signature share a common PIN while all other keys share another PIN (synchronized)
unique	0x03	All four AppUsage types must have different PINs while keys with the same AppUsage share a common PIN (synchronized)

Note that keys having a shared PIN groping attribute must be treated as having a single virtual PIN error counter, while signature+standard implies two separate error counters. “Synchronized” means that a PIN value or status change must propagate to all keys sharing the PIN.

## Key Application Usage
The AppUsage attribute specifies what applications keys are intended for according to the following table:
KeyGen2 Name	Value	Comment
signature	0x00	The key should only be used in signature applications like S/MIME
authentication	0x01	The key should only be used in applications like TLS client certificate authentication and login to AD (Active Directory)
encryption	0x02	The key should only be used in encryption applications
universal	0x03	There are no restrictions on key usage

Enforcement of AppUsage is up to each application to perform.
Note that AppUsage must not constrain a key's internal use of cryptographic algorithms in any way, because for that purpose there is the EndorsedAlgorithm mechanism.
Although AppUsage could be be regarded as a duplication of the X.509 key usage and extended key usage attributes the latter have proved hard to use as “filters” to certificate selection GUIs. AppUsage is also applicable for other credentials like OTPs (One Time Passwords) and Information Cards.
However, an equally important target for AppUsage is that in conjunction with PIN Grouping provide the means for aiding users in PIN input GUIs in the case an issuer requires separate PINs for different keys and applications.
The following matrix shows the recommended interpretation of PIN GUI “hints”:

PIN Grouping	signature	authentication	encryption	universal
none	PIN	PIN	PIN	PIN
shared	PIN	PIN	PIN	PIN
signature+standard	Signature PIN	PIN	PIN	PIN
unique	Signature PIN	Authentication PIN	Encryption PIN	PIN

For this scheme to work a prerequisite is (of course) that the middleware is specifically adapted for SKS.
## Biometric Protection
An SKS may also support using biometric data as an alternative to PINs. See getDeviceInfo. The following table shows the biometric protection options as defined by the BiometricProtection policy attribute:
KeyGen2 Name	Value	Comment
none	0x00	No biometric protection
alternative	0x01	The key may be authorized with a PIN or by biometrics
combined	0x02	The key is protected by a PIN and by biometrics
exclusive	0x03	The key is only protected by biometrics

Note that there is no API support for biometric authentication, such information is typically provided through GPIO (General Purpose Input Output) ports between the biometric sensor and the SKS. The type of biometrics used is outside the scope of SKS and is usually established during enrollment.
The biometric protection option is only intended to be applied to User API methods like signHashedData.

# Data Types
The table below shows the data types used by the SKS API. Note that multi-byte integers must be stored in big-endian fashion whenever they are serialized like in MAC operations. Also see Method List.
Type	Length	Comment
byte	1	Unsigned byte (0 - 0xFF)
bool	1	Byte containing 0x01 (true) or 0x00 (false)
short	2	Unsigned two-byte integer (0 - 0xFFFF)
int	4	Unsigned four-byte integer (0 - 0xFFFFFFFF)
byte[ ]	2 + length	Array of bytes with a leading “short” holding the length of the data
blob	4 + length	Long array of bytes with a leading “int” holding the length of the data
id	2 + length	Special form of byte[ ] which must contain an 1-32 byte string according to the XML Schema data type NCName but restricted to: | a-z | A-Z | 0-9 | . | _ | - |
uri	2 + length	UTF-8 encoded byte[ ] array which must not exceed 1000 bytes

If an array is followed by a number in brackets (byte[32]) it means that the array must be exactly of that length.
Variables and literals that represent textual data must be UTF-8 encoded and not include terminating null characters; they are in this specification considered equivalent to byte[ ].
Note that length indicators are only applicable to array objects when included in MAC operations, or when they are serialized.
# Method List
This section provides a list of the SKS methods. The number in parenthesis denotes the decimal value used to identify the method in a call. Method calls are formatted as strings of bytes where the first byte holds the method ID and the succeeding bytes the applicable argument data. User API methods have method IDs ≥ 100.
Note: The described API is adapted for an SKS using low-level byte-streams for communication. However, the SKS design is equally applicable to API schemes using high-level objects and exceptions. The only thing that must remain intact are the cryptographic operations including how objects are represented in MACs.

Note that a KeyHandle in this specification always refers to a key entry. See Key Entries.

# Return Values
All methods return a single-byte status code. In case the status is <> 0 there is an error and any expected succeeding values must not be read as they are not supposed to be available. Instead there must be a second return value containing a UTF-8 encoded description in English to be used for logging and debugging purposes as shown below:
Name	Type	Comment
Status	byte	Non-zero (error) value
ErrorString	byte⁮[ ]	A human-readable error description

# Error Codes
The following table shows the standard SKS error-codes:
Name	Value	Comment
ERROR_AUTHORIZATION	0x01	Non-fatal error returned when there is something wrong with a supplied PIN or PUK code. See getKeyProtectionInfo
ERROR_NOT_ALLOWED	0x02	Operation is not allowed
ERROR_STORAGE	0x03	No persistent storage available for the operation
ERROR_MAC	0x04	MAC does not match supplied data
ERROR_CRYPTO	0x05	Various cryptographic errors
ERROR_NO_SESSION	0x06	Provisioning session not found
ERROR_NO_KEY	0x07	Key not found
ERROR_ALGORITHM	0x08	Unknown or non-matching algorithm
ERROR_OPTION	0x09	Invalid or unsupported option
ERROR_INTERNAL	0x0A	Internal error

## getDeviceInfo (1)
Input
Name	Type	Comment
This method does not have any input arguments

Output
Name	Type	Comment
Status	byte	See Return Values
APILevel	short	0x0001 => Applies to this API specification
UpdateURL	uri	URL pointing to a firmware update center or if not applicable a zero length array
VendorName	byte⁮[ ]	1-128 byte string holding the name of the vendor
VendorDescription	byte⁮[ ]	1-128 byte string holding a vendor description of the SKS device
PathLength	byte	Non-zero value holding the number of X509Certificate objects
X509Certificate...	byte⁮[ ]	DER encoded X.509 certificate object repeated as defined by PathLength
Algorithms	short	Non-zero value holding the number of Algorithm objects
Algorithm...	uri	Algorithm URI repeated as defined by Algorithms. See Algorithm Support
RSAExponentSupport	bool	True if the issuer may specify an explicit exponent value. See RSAExponent
RSAKeySizes	byte	Non-zero value holding the number of RSAKeySize objects
RSAKeySize...	short	Holds an RSA key size in bits and is repeated as defined by RSAKeySizes. See Algorithm Support
CryptoDataSize	int	Maximum number of bytes in the Data argument of cryptographic methods
ExtensionDataSize	int	Maximum size of ExtensionData objects
DevicePINSupport	bool	True if the SKS supports a device PIN. See createKeyPair
BiometricSupport	bool	True if the SKS supports biometric authentication options. See Biometric Protection

getDeviceData lists the core characteristics of an SKS which is used by provisioning schemes like KeyGen2.
The X509Certificate objects must form an ordered and contiguous certificate path so that the first object contains the actual SKS Device Certificate. The path does though not have to be complete (include all upper-level CAs).
RSAKeySizes must be specified in ascending order.
A compliant SKS must support ExtensionData objects with a size of at least 65536 bytes.
A compliant SKS must support a CryptoDataSize of at least 16384 bytes.
For ECC key generation see Elliptic Curves.
## createProvisioningSession (2)
Input
Name	Type	Comment
Algorithm	uri	Session creation algorithm URI. See next page
ServerSessionID	id	Server-created provisioning ID which should be unique for each session
ServerEphemeralKey	byte[ ]	Server-created ephemeral ECDH key. See ServerEphemeralKey
IssuerURI	uri	URI associated with the issuer. See IssuerURI
KeyManagementKey	byte[ ]	Key management key or zero length array. See KeyManagementKey
ClientTime	int	Locally acquired time in UNIX “epoch” format in seconds. See ClientTime
SessionLifeTime	int	Validity of the provisioning session in seconds
SessionKeyLimit	short	Upper limit of SessionKey operations. See SessionKeyLimit

Output
Name	Type	Comment
Status	byte	See Return Values
ClientSessionID	id	SKS-created provisioning ID which must be unique for each session
ClientEphemeralKey	byte[ ]	SKS-created ephemeral ECDH key which must be in X.509 DER format
Attestation	byte[ ]	Session creation attestation signature
ProvisioningHandle	int	Local handle to created provisioning session

createProvisioningSession establishes a persistent session key that is only known by the issuer and the SKS for usage in subsequent provisioning steps. In addition, the SKS is optionally authenticated by the issuer.

Continued on the next page...

Shown below is the mandatory to support SKS session key creation algorithm:
http://xmlns.webpki.org/keygen2/1.0#algorithm.sks.s1
Generate a for this SKS unique ClientSessionID / Output ClientSessionID / Generate an ephemeral ECDH key-pair EKP using the same named curve as ServerEphemeralKey / Output ClientEphemeralKey = EKP.PublicKey / Apply the SP800-56A ECC CDH primitive on EKP.PrivateKey and ServerEphemeralKey creating a shared secret Z / Define internal variable: byte[32] SessionKey / Set SessionKey = HMAC-SHA256 (Z, ClientSessionID || // KDF (Key Derivation Function) ServerSessionID || IssuerURI || Device Certificate) / Output Attestation = Sign (Attestation Private Key, // See Architecture HMAC-SHA256 (SessionKey, Algorithm || ServerEphemeralKey || EKP.PublicKey || KeyManagementKey || ClientTime || SessionLifeTime || SessionKeyLimit)) / Define internal variable: short MACSequenceCounter and set it to zero / Store SessionKey, MACSequenceCounter, ClientSessionID, ServerSessionID, IssuerURI, KeyManagementKey, ClientTime, SessionLifeTime and SessionKeyLimit in the Credential Database and return a handle to the database entry in ProvisioningHandle / Output ProvisioningHandle / Note that individual elements featured in the argument (e.g. ClientSessionID) to the HMAC operations must be represented as described in Data Types.

Creation of a session key is an atomic operation.

Continued on the next page...
Remarks
If any succeeding operation in the same provisioning session, is regarded as incorrect by the SKS, the session must be terminated and removed from internal storage including all associated data created in the session.
An SKS should only constrain the number of simultaneous sessions due to lack of storage.
A provisioning session should not be terminated due to power down of an SKS.
Algorithm defines the creation of SessionKey but also the integrity, confidentiality, and attestation mechanisms used during the provisioning session. See Session Security Mechanisms.
Using KeyGen2 IssuerURI is the URL to which the result of this method is POSTed.
ServerEphemeralKey must be in X.509 DER format and must match the Elliptic Curves capabilities given by getDeviceInfo.
The Sign function must use PKCS #1 RSASSA signatures for RSA keys and ECDSA for ECC keys with SHA256 as the hash function. The distinction between RSA and ECDSA keys is performed through the Device Certificate (see getDeviceInfo) which in KeyGen2 is supplied as well as a part of the response to the issuer.
ProvisioningHandle must be static, unique and never be reused.
When ClientTime is transferred through a protocol such as KeyGen2 it must always as a minimum have seconds resolution otherwise serious interoperability issues will occur. Possible milliseconds must though be truncated during the HMAC calculation.
The SessionKeyLimit attribute must be large enough to handle all SessionKey related operations required during the rest of the provisioning session, otherwise the session must be terminated. See Session Security Mechanisms. Note that methods like setSymmetricKey and pp_deleteKey actually use two SessionKey operations.
A KeyManagementKey must be supplied if provisioned objects should be updatable in a future session (see pp_deleteKey, pp_updateKey, and pp_cloneKeyProtection), else this item must be a zero-length array. The KeyManagementKey must either be an RSA or an ECDSA public key in X.509 DER format, compatible with the SKS Algorithm Support.

Continued on the next page...

On the server side the following should be performed:

Server Response Validation
Decide if DeviceCertificatePath of ProvisioningInitializationResponse is to be accepted/trusted. / Run the the same SP800-56A procedure and KDF as for the SKS but now using ClientEphemeralKey and the saved private key of ServerEphemeralKey to obtain SessionKey / VerifySignature (Device Certificate.PublicKey, // Received Attestation, // Received HMAC-SHA256 (SessionKey, Algorithm || // Saved ServerEphemeralKey || // Saved ClientEphemeralKey || // Received KeyManagementKey || // Saved ClientTime || // Received SessionLifeTime || // Saved SessionKeyLimit)) // Saved

If all tests above succeed the issuer server may continue with the actual provisioning process.

Continued on the next page...
When using KeyGen2 the input to createProvisioningSession is expressed as shown in the fragment below:
<ProvisioningInitializationRequest ID="_0fa47ab3c00c … a67992b6ac61c" SubmitURL="https://ca.example.com/enroll" SessionLifeTime="50000" SessionKeyLimit="25" Algorithm="http://xmlns.webpki.org/keygen2/1.0#algorithm.sks.s1" … > / <ServerEphemeralKey> <ds11:ECKeyValue> / <ds11:NamedCurve URI="urn:oid:1.2.840.10045.3.1.7"/> / <ds11:PublicKey>JK/mSALhBpUjjPAe/ … fXG8z17eZV3mVDZTBM</ds11:PublicKey> / </ds11:ECKeyValue> / </ServerEphemeralKey> <KeyManagementKey> / <ds:RSAKeyValue> <ds:Modulus>ALhBpUjJK/mSjPAe/ … fXG8z1V3mVDZTBM7eZ</ds:Modulus> <ds:Exponent>AQAB</ds:Exponent> </ds:RSAKeyValue> / </KeyManagementKey> / </ProvisioningInitializationRequest>

Note: The KeyManagementKey element is optional.

The table below illustrates argument mapping:
KeyGen2 Element	SKS Counterpart
ProvisioningInitializationRequest@ID	ServerSessionID
ProvisioningInitializationRequest@SubmitURL	IssuerURI
ProvisioningInitializationRequest@SessionLifeTime	SessionLifeTime
ProvisioningInitializationRequest@SessionKeyLimit	SessionKeyLimit
ProvisioningInitializationRequest@Algorithm	Algorithm
ServerEphemeralKey/ECKeyValue	ServerEphemeralKey
KeyManagementKey	KeyManagementKey
N/A - Gathered by the local provisioning middleware	ClientTime

Continued on the next page...
When using KeyGen2 the output from createProvisioningSession is translated as shown in the fragment below:
<ProvisioningInitializationResponse ID="_126992b6 … a8a6b484db8f" / ServerSessionID="_0fa47ab3c00c … a67992b6ac61c" ClientTime="2010-03-18T11:23:29Z" ServerCertificateFingerprint="AvDWx6xbg3GDGzdz … yJk8Js0Oul+Ba/Xc8=" Attestation="Ob7MvaXC/rNx/rkNZJEo … 8lch/6sngIszfpElrggQfl" … > / <ClientEphemeralKey> <ds11:ECKeyValue> / <ds11:NamedCurve URI="urn:oid:1.2.840.10045.3.1.7"/> / <ds11:PublicKey>PRZre90SQLp … 16m9FokKxV3F40Y=</ds11:PublicKey> / </ds11:ECKeyValue> / </ClientEphemeralKey> <DeviceCertificatePath> / <ds:X509Data> / <ds:X509Certificate>MIIC2TCCAcGgAwIBAg ... hugc53W4nNzggt2w==</ds:X509Certificate> / </ds:X509Data> / </DeviceCertificatePath> / <ds:Signature> / <ds:SignedInfo> / <ds:CanonicalizationMethod Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/> / <ds:SignatureMethod Algorithm="http://www.w3.org/2001/04/xmldsig-more#hmac-sha256"/> / <ds:Reference URI="#_126992b6 … a8a6b484db8f"> / <ds:Transforms> / <ds:Transform Algorithm="http://www.w3.org/2000/09/xmldsig#enveloped-signature"/> / <ds:Transform Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/> / </ds:Transforms> / <ds:DigestMethod Algorithm="http://www.w3.org/2001/04/xmlenc#sha256"/> / <ds:DigestValue>yLD0zNA48Xt9xXNHuBUlK0hL51zn0SYj2IfDXm42PLc=</ds:DigestValue> / </ds:Reference> / </ds:SignedInfo> / <ds:SignatureValue>aRiSdmrn/KgtjqtTReF+6DOuIemRuw2xV9yuOPAlMj8=</ds:SignatureValue> / <ds:KeyInfo> / <ds:KeyName>derived-session-key</ds:KeyName> / </ds:KeyInfo> / </ds:Signature> / </ProvisioningInitializationResponse>

The table below illustrates mapping:
KeyGen2 Element	SKS Counterpart
ProvisioningInitializationResponse@ID	ClientSessionID
ProvisioningInitializationResponse@ServerSessionID	Input.ServerSessionID
ProvisioningInitializationResponse@ClientTime	Input.ClientTime
ProvisioningInitializationResponse@Attestation	Attestation
ClientEphemeralKey/ECKeyValue	ClientEphemeralKey
DeviceCertificatePath/X509Data/X509Certificate	Certificate path from getDeviceInfo
Signature/SignatureValue	Created with signProvisioningSessionData

Apart from needed for verifying the Attestation signature the DeviceCertificatePath identifies the SKS. The Signature element holds a standard WC3 enveloped XML Signature. Also see Security Considerations.
## closeProvisioningSession (3)
Input
Name	Type	Comment
ProvisioningHandle	int	Local handle to an open provisioning session
Nonce	byte[ ]	Server generated 1-32 byte nonce value
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values
Attestation	byte[32]	Session termination attestation signature. See Attestations

closeProvisioningSession terminates a provisioning session and returns a proof of successful operation to the issuer. However, success status must only be returned if all of the following conditions are valid:
- There is an open provisioning session associated with ProvisioningHandle
- The MAC computes correctly using the method described in MAC Operations where Data is arranged as follows:
  Data = ClientSessionID || ServerSessionID || IssuerURI || Nonce
- All generated keys are fully provisioned which means that matching public key certificates have been deployed.
  See setCertificatePath
- EndorsedAlgorithm URIs match the provisioned key material with respect to symmetric or asymmetric operations as well as to length. Asymmetric keys are also tested for RSA and ECC algorithm compliance
- There are no unreferenced PIN or PUK policy objects. See createPUKPolicy and createPINPolicy
- The post provisioning operations succeed during the final commit. See Transaction Based Operation
If verification is successful, closeProvisioningSession must also reassign provisioning session ownership to the current (closing) session for all objects belonging to sessions that have been subject to a post provisioning operation. The original session objects must subsequently be deleted since they have no mission anymore. Also see Provisioning Objects.
If verification fails, all objects created in the session must be deleted and post provisioning operations must be rolled back.
When a provisioning session has been successfully closed by this method, it remains stored until all associated keys have been deleted.
Using KeyGen2 closeProvisioningSession is invoked as the last step of processing ProvisioningFinalizationRequest where the top element holds the associated MAC and Nonce attributes.

The Attestation object is created by attesting the following Data:
Data = Input.MAC || Algorithm
Also see SessionKeyLimit.

A successful KeyGen2 response would typically look like:

<ProvisioningFinalizationResponse ID="_126992b6 … a8a6b484db8f" ServerSessionID="_0fa47ab3c00c … a67992b6ac61c" Attestation="gEWzCCD ... 0w81L/ls2W0UYNE=" … />

## enumerateProvisioningSessions (4)
Input
Name	Type	Comment
ProvisioningHandle	int	Input enumeration handle
ProvisioningState	bool	If true list only open provisioning sessions. If false list only closed dittos

Output
Name	Type	Comment
Status	byte	See Return Values
ProvisioningHandle	int	Output enumeration handle
The following elements must only be emitted if ProvisioningHandle <> 0xFFFFFFFF
KeyManagementKey	byte[ ]	See createProvisioningSession
ClientTime	int
SessionLifeTime	int
ServerSessionID	id
ClientSessionID	id
IssuerURI	uri

enumerateProvisioningSessions is primarily intended to be used by provisioning middleware for retrieving handles to open provisioning sessions in sessions that are interrupted due to a certification process or similar.
In addition, users of portable SKSes (like smart cards), may carry out provisioning steps on different computers through this method.
enumerateProvisioningSessions may also be useful for debugging and “cleaning” purposes.
The input ProvisioningHandle is initially set to 0xFFFFFFFF to start an enumeration round.
Succeeding calls should use the output ProvisioningHandle as input to the next call.
When enumerateProvisioningSessions returns with a ProvisioningHandle = 0xFFFFFFFF there are no more provisioning objects to read.
## abortProvisioningSession (5)
Input
Name	Type	Comment
ProvisioningHandle	int	Local handle to an open provisioning session

Output
Name	Type	Comment
Status	byte	See Return Values

abortProvisioningSession is intended to be used by provisioning middleware if an unrecoverable error occurs in the communication with the issuer, or if a user cancels a session. If there is a matching and still open provisioning session, all associated data must be removed from the SKS, otherwise an error must be returned.
## signProvisioningSessionData (6)
Input
Name	Type	Comment
ProvisioningHandle	int	Local handle to an open provisioning session
Data	byte[ ]	Data to be signed

Output
Name	Type	Comment
Status	byte	See Return Values
Result	byte[32]	Signed data

signProvisioningSessionData signs arbitrary data that is supplied by the provisioning middleware.
The purpose of signProvisioningSessionData is adding data integrity to provisioning messages from clients to issuers.
The signature scheme is as follows:
Result = HMAC-SHA256 (SessionKey || "External Signature", Data)
Note that Data must be used “as is” in the HMAC operation, excluding length information.
A relying party must distinguish between such signatures and Attestations since only the latter are actually vouched for by the SKS.
Also see SessionKeyLimit.
## createPUKPolicy (7)
Input
Name	Type	Comment
ProvisioningHandle	int	Local handle to an open provisioning session
ID	id	External name of the PUK policy object. See Object IDs
PUKValue	byte[ ]	Encrypted PUK value. See Encrypted Data
Format	byte	Format of PUK strings. See PIN and PUK Formats
RetryLimit	short	Number of incorrect PUK values (in a sequence), forcing the PUK object to permanently lock up. A zero value indicates that there is no limit but that the SKS will introduce an internal 1‑10 second delay before acting on an unlock operation in order to thwart exhaustive attacks
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values
PUKPolicyHandle	int	Non-zero handle to created PUK policy object

createPUKPolicy creates a PUK policy object in the Credential Database to be referenced by subsequent calls to the createPINPolicy method.
The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = ID || PUKValue || Format || RetryLimit
Note that PUKValue is MACed in encrypted form and then decrypted by the SKS before storing.
The purpose of a PUK is to facilitate a master key for unlocking keys that have locked-up due to faulty PIN entries. See unlockKey.
PUK policy objects are not directly addressable after provisioning; in order to read PUK policy data, you need to use an associated key handle as input. See getKeyProtectionInfo.

## createPINPolicy (8)
Input
Name	Type	Comment
ProvisioningHandle	int	Local handle to an open provisioning session
ID	id	External name of the PIN policy object. See Object IDs
PUKPolicyHandle	int	Handle to a governing PUK policy object or zero
UserDefined	bool	True if PINs belonging to keys governed by the PIN policy are supposed to be set by the user or by the issuer. See PINValue
UserModifiable	bool	True if PINs can be changed by the user after provisioning
Format	byte	Format of PIN strings. See PIN and PUK Formats
RetryLimit	short	Non-zero value holding the number of incorrect PIN values (in a sequence), forcing a key to lock up
Grouping	byte	See PIN Grouping
PatternRestrictions	byte	See PIN Patterns
MinLength	short	Minimum decoded PIN length in bytes. See PIN and PUK Formats
MaxLength	short	Maximum decoded PIN length in bytes. See PIN and PUK Formats
InputMethod	byte	See PIN Input Methods
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values
PINPolicyHandle	int	Non-zero handle to created PIN policy object

createPINPolicy creates a PIN policy object in the Credential Database to be referenced by subsequent calls to the createKeyPair method.
The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = ID || PUKReference || UserDefined || UserModifiable || Format || RetryLimit ||
        Grouping || PatternRestrictions || MinLength || MaxLength || InputMethod
PUKReference is set to "#N/A" if PUKPolicyHandle is zero, else it is set to the ID of the referenced PUK policy object.
If PUKPolicyHandle is zero no PUK is associated with the PIN policy object.
PIN policy objects are not directly addressable after provisioning; in order to read PIN policy data, you need to use an associated key handle as input. See getKeyProtectionInfo.

## createKeyPair (9)
Input
Name	Type	Comment
ProvisioningHandle	int	Local handle to an open provisioning session
ID	id	External name of the key. See Object IDs
Algorithm	uri	Key generation and attestation algorithm URI. See next page
ServerSeed	byte⁮[32]	Server input to the random number generation process. See ServerSeed
DevicePINProtection	bool	True if the key is to be protected by a device pin. / See Key Protection Objects
PINPolicyHandle	int	Handle to a governing PIN policy object or zero. See createPINPolicy
PINValue	byte⁮[ ]	See PINValue, PIN Patterns and PIN Grouping
BiometricProtection	byte	See Biometric Protection
PrivateKeyBackup	bool	True if the generated private key is to be output in PrivateKey for backup by the issuer
ExportProtection	byte	See Key Export
DeleteProtection	byte	See Key Delete
EnablePINCaching	bool	True if middleware may cache PINs for this key
AppUsage	byte	See Key Application Usage
FriendlyName	byte⁮[ ]	String of 0-128 bytes that will be associated with this key for use in GUIs
KeyAlgorithmType	byte	Type of key to be generated: 0x00 = RSA, 0x01 = ECC
The following two elements must only be set for RSA keys
RSAKeySize	short	RSA key size in bits. See getDeviceInfo
RSAExponent	int	Zero (use default) or a defined exponent. See getDeviceInfo
The following element must only be set for ECC keys
NamedCurve	uri	Curve name URI. See Elliptic Curves
EndorsedAlgorithms	byte	Value [0..255] holding the number of EndorsedAlgorithm URIs
EndorsedAlgorithm...	uri	Endorsed algorithm URI repeated as defined by EndorsedAlgorithms
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values
KeyHandle	int	Local handle to created key-pair object
PublicKey	byte⁮[ ]	Generated public key in X.509 DER representation
Attestation	byte⁮[ ]	See Attestation
PrivateKey	byte⁮[ ]	Optional: Encrypted generated private key. See PrivateKey

createKeyPair generates an asymmetric key-pair in the Credential Database according to the issuer's specification.

Continued on the next page...
The following operations match the mandatory to support key generation and attestation algorithm: http://xmlns.webpki.org/keygen2/1.0#algorithm.sks.k1

The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = ID || Algorithm || ServerSeed || PINPolicyReference || PINValueReference ||
        BiometricProtection || PrivateKeyBackup || ExportProtection || DeleteProtection ||
        EnablePINCaching || AppUsage || FriendlyName || KeySpecifier [|| EndorsedAlgorithm...]
PINPolicyReference is set to "#Device PIN" if DevicePINProtection is true, to "#N/A" if PINPolicyHandle is zero, else it is set to the ID of the referenced PIN policy object.
PINValueReference is set to "#N/A" if PINPolicyHandle is zero, or if DevicePINProtection is true, or if the PIN is UserDefined, else it is set to the encrypted PINValue.
KeySpecifier denotes the sequence consisting of KeyAlgorithmType and its related parameters in the same order and format as in the API. That is, an RSA 1024 bit key specifier would be represented by: 0x00 0x04 0x00 0x00 0x00 0x00 0x00.

Attestation vouches for that generated key-pairs actually reside in the SKS by attesting (see Attestations) keys according to the following Data scheme:
Data = ID || PublicKey [|| PrivateKey]
Note that the encrypted PrivateKey must only be used in the attestation Data if actually emitted.

Remarks
KeyHandle must be static, unique and never be reused. Note that a KeyHandle returned by createKeyPair must not be featured in User API operations until the associated provisioning session has been closed (see closeProvisioningSession).
Object IDs for createKeyPair, createPINPolicy and createPUKPolicy share a common namespace but the namespace is entirely local to the provisioning session. Although only static identifiers are used in the examples, Object IDs may be randomized to increase entropy of MAC Operations.
A compliant SKS should use 65537 as the default RSA exponent value.
How ServerSeed is applied to the random number generation process is unspecified. The only requirement is that it must not be able to reduce the entropy.
A non-zero BiometricProtection value presumes that the target SKS supports Biometric Protection, otherwise an error must be returned. See getDeviceInfo.
The PrivateKey element must only be supplied if PrivateKeyBackup is true. If PrivateKey is present it must hold the generated private key in PKCS #8 format but wrapped as described in Encrypted Data.
EndorsedAlgorithm URIs must be sorted in ascending alphabetical order before calling createKeyPair.
EndorsedAlgorithm URIs must be checked for compatibility with Algorithm Support.
EndorsedAlgorithm compliance must be enforced by the User API.
EndorsedAlgorithm URIs must not be checked against actual key material during createKeyPair. This check must be deferred to closeProvisioningSession.
If no EndorsedAlgorithm URIs are specified, the key is only constrained by the key material.
With the special algorithm http://xmlns.webpki.org/keygen2/1.0#algorithm.none (which is only permitted as a single EndorsedAlgorithm item), keys must be disabled from executing cryptographic operations through the User API.

Continued on the next page...
A set DevicePINProtection presumes that the target SKS supports a “device PUK/PIN”, otherwise an error must be returned. The characteristics of device PINs are out of scope for the SKS specification. See getDeviceInfo.
DevicePINProtection must not be combined with local PIN policy objects.
The PINValue object must be set by the caller as illustrated by the following pseudo code:
if (PINPolicyHandle == 0) // No PIN or device PIN
  {
     PINValue = zero length array;
  }
else if (PINPolicyHandle.UsedDefined) // see UserDefined
  {
     PINValue = user-defined clear text PIN value; // taken from a local provisioning GUI
  }
else
  {
     PINValue = encrypted issuer-set PIN value; // see Encrypted Data
  }

Continued on the next page...
The following XML extract shows a typical key generation (initialization) request in KeyGen2:
<KeyInitializationRequest Algorithm="http://xmlns.webpki.org/keygen2/1.0#algorithm.sks.k1" … > <PUKPolicy ID="PUK.1" Format="numeric" RetryLimit="3" Value="mjRuO …1Oqw" MAC="uPqE ... HlF="> <PINPolicy ID="PIN.1" Format="numeric" Grouping="shared" MaxLength="8" MinLength="4" PatternRestrictions="three-in-a-row sequence" RetryLimit="3" MAC="gz56 ... 2B7="> <KeyPair ID="Key.1" AppUsage="authentication" MAC="nFRuPgz ... H2B429S="> <EC NamedCurve="urn:oid:1.2.840.10045.3.1.7"/> </KeyPair> <KeyPair ID="Key.2" AppUsage="encryption" PrivateKeyBackup="true" MAC="gSg4chh ... H2BEE7="> <RSA KeySize="2048"/> </KeyPair> </PINPolicy> </PUKPolicy> / </KeyInitializationRequest>

This sequence should be interpreted as a request for an ECC key and an RSA key where both keys are protected by a single (shared) user-defined (within the specified policy limits) PIN. The PIN is in turn governed by an issuer-defined, protocol wise secret PUK. In addition, private key backup was requested for the RSA key.
In the sample KeyGen2 default values have been utilized which is why there are few visible key generation attributes.

When using KeyGen2 the output from createKeyPair is translated as shown in the fragment below:
<KeyInitializationResponse … > / <PublicKey ID="Key.1" Attestation="X2oMtrm8rRL … XyTvPuTbergHfnJw=="> <ds11:ECKeyValue> / <ds11:NamedCurve URI="urn:oid:1.2.840.10045.3.1.7"/> / <ds11:PublicKey>BMUY+QiZdFJyzozMgQqA … ptPGNy/LcDVSXx7s/Y=</ds11:PublicKey> / </ds11:ECKeyValue> </PublicKey> <PublicKey ID="Key.2" Attestation="TbergHftrm8rRL … wyTvPX2XoMunJ=="> / <ds:RSAKeyValue> <ds:Modulus>ALhBpUjJK/mSjPAe/ … fXG8z1V3mVDZTBM7eZ</ds:Modulus> <ds:Exponent>AQAB</ds:Exponent> </ds:RSAKeyValue> / <PrivateKey>lysZRM+dYS+bFn5 … fvJLE6lJq7yshOIZTp</PrivateKey> </PublicKey> / </KeyInitializationResponse>

A conforming server must after receival of the response verify that the number and IDs of returned keys match the request. In addition, each returned key must be checked for correctness regarding attestation data and that the generated public key actually complies with that of the request.
## getKeyHandle (10)
Input
Name	Type	Comment
ProvisioningHandle	int	Local handle to an open provisioning session
ID	id	See createKeyPair

Output
Name	Type	Comment
Status	byte	See Return Values
KeyHandle	int	Local handle to a key belonging to an open provisioning session

getKeyHandle returns a KeyHandle based on the provisioning session specific key ID.
An invalid key must return an error and abort the provisioning session.
## setCertificatePath (11)
Input
Name	Type	Comment
KeyHandle	int	Local handle to a key-pair belonging to an open provisioning session
PathLength	byte	Non-zero value holding the number of X509Certificate objects in the call
X509Certificate...	byte⁮[ ]	DER encoded X.509 certificate object repeated as defined by PathLength‪‫‬‭‪‏‪‏‎
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values

setCertificatePath attaches an X.509 certificate path to an already created key-pair. See createKeyPair.
The X509Certificate objects must form an ordered and contiguous certificate path so that the first object contains the
End-Entity Certificate usually holding the public key of the target key‑pair. The path does though not have to be complete (include all upper-level CAs). Path validity should be verified by the provisioning middleware before calling this method.
Individual X509Certificate objects must not exceed CryptoDataSize.
Note that an SKS must not not attempt to verify that the End-Entity Certificate and KeyHandle.PublicKey match because that would disable the restorePrivateKey method. It is the MAC operation that is facilitating a cryptographically verifiable binding between the certificate path and the designated key entry.
The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = KeyHandle.PublicKey || KeyHandle.ID || X509Certificate...

Although not recommended for serious deployments, a compliant SKS must accept multiple key entries being associated by the same End-Entity Certificate.
The provisioning middleware should verify that the public key of the End-Entity Certificate matches the algorithmic capabilities of the SKS. See Algorithm Support.

Continued on the next page...

The following KeyGen2 fragment shows its interaction with setCertificatePath:
<ProvisioningFinalizationRequest ClientSessionID="_126992b6 … a8a6b484db8f" ID="_0fa47ab3c00c … a67992b6ac61c" MAC="GcaqnRxW ... 8kabXDgWr=" Nonce="aqnPb6x0 ... kms34gfW2=" … > / <CertficatePath ID="Key.1" MAC="ngSgmRuPE ... HlFWrM421wY="> <ds:X509Data> <ds:X509Certificate>MIIC2TCCAcGgAwIBAgS … NRT+VokJJsBecyALgeT0Dw==</ds:X509Certificate> </ds:X509Data> </CertficatePath> / </ProvisioningFinalizationRequest>

The table below illustrates argument mapping:
KeyGen2 Element	SKS Counterpart
CertficatePath@ID	KeyHandle.ID
CertficatePath@MAC	MAC
CertficatePath/X509Data/X509Certificate...	X509Certificate...

The owning ProvisioningHandle and local KeyHandle can be retrieved by calling enumerateProvisioningSessions and getKeyHandle respectively. The request attributes ProvisioningFinalizationRequest@ClientSessionID and ProvisioningFinalizationRequest@ID hold the ClientSessionID and ServerSessionID of the provisioning session.
## setSymmetricKey (12)
Input
Name	Type	Comment
KeyHandle	int	Local handle to a key belonging to an open provisioning session
SymmetricKey	byte⁮[ ]	“Piggybacked” symmetric key encrypted as described in Encrypted Data
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values

setSymmetricKey imports and links a symmetric key to an already created key-pair and certificate.
The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = End-Entity Certificate || SymmetricKey
Note that SymmetricKey objects must be MACed in encrypted form and then decrypted by the SKS before storing.
Symmetric keys must not exceed 128 bytes.
With the special EndorsedAlgorithm http://xmlns.webpki.org/keygen2/1.0#algorithm.none arbitrary static shared secrets can be specified. When used together with exportKey, a suitable PIN policy and a PropertyBag object holding site information, an SKS could then also serve as a browser password store.
After setSymmetricKey has been called the key entry is marked as “symmetric”. That is, the private key is disabled as well as all operations associated with it See getKeyAttributes.

Continued on the next page...

The following KeyGen2 fragments show the “piggyback” arrangement. First the server issues a key-pair request:

<KeyInitializationRequest Algorithm="http://xmlns.webpki.org/keygen2/1.0#algorithm.sks.k1" … > <PUKPolicy ID="PUK.1" Format="numeric" RetryLimit="3" Value="mjRuO …1Oqw" MAC="uPqE ... HlF="> <PINPolicy ID="PIN.1" Format="numeric" MaxLength="8" MinLength="4" PatternRestrictions="three-in-a-row sequence" RetryLimit="3" MAC="gz56 ... 2B7="> <KeyPair ID="Key.1" AppUsage="authentication" / EndorsedAlgorithms="http://www.w3.org/2000/09/xmldsig#hmac-sha1" / MAC="gSg4chh ... H2BEE7="> <RSA KeySize="1024"/> </KeyPair> </PINPolicy> </PUKPolicy> / </KeyInitializationRequest>

The request above is identical to requests for PKI except for the optional EndorsedAlgorithm declaration which in the sample limited symmetric key operations to HMAC-SHA1.

After the request the client generates a compatible key-pair response which is identical to that of PKI:

<KeyInitializationResponse … > / <PublicKey ID="Key.1" Attestation="TbergHftrm8rRL … wyTvPX2XoMunJ=="> / <ds:RSAKeyValue> <ds:Modulus>ALhBpUjJK/mSjPAe/ … fXG8z1V3mVDZTBM7eZ</ds:Modulus> <ds:Exponent>AQAB</ds:Exponent> </ds:RSAKeyValue> / </PublicKey> / </KeyInitializationResponse>

The server then responds with the usual certificated public key plus an encrypted “piggybacked” symmetric key:

<ProvisioningFinalizationRequest ClientSessionID="_126992b6 … a8a6b484db8f" ID="_0fa47ab3c00c … a67992b6ac61c" MAC="GcaqnRxW ... 8kabXDgWr=" Nonce="aqnPb6x0 ... kms34gfW2=" … > / <CertficatePath ID="Key.1" MAC="ngSgmRuPE ... HlFWrM421wY="> <ds:X509Data> <ds:X509Certificate>MIIC2TCCAcGgAwIBAgS … NRT+VokJJsBecyALgeT0Dw==</ds:X509Certificate> </ds:X509Data> <SymmetricKey MAC="je7KiznTll … vInumZCjxSl1=">vInt09Esmg94v ... YU3tgIdhcNNby</SymmetricKey> </CertficatePath> / </ProvisioningFinalizationRequest>

For details on how to map keys and sessions, see setCertificatePath.
Note that the X.509 certificate serves as a universal key ID. That is, SKS treats asymmetric and symmetric keys close to identically.
## addExtension (13)
Input
Name	Type	Comment
KeyHandle	int	Local handle to a key belonging to an open provisioning session
Type	uri	Type URI. Holds a unique name identifying the extension type
SubType	byte	See table below
Qualifier	byte⁮[ ]	See table below
ExtensionData	blob	Extension object. Regarding size constraints see getDeviceInfo
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values

addExtension adds attribute (extension) data to an already created key-pair and certificate.
The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = End-Entity Certificate || Type || SubType || Qualifier || ExtensionData

The following table shows SubType, Qualifier and ExtensionData mapping using KeyGen2:
KeyGen2 Element	SubType	Qualifier	ExtensionData
Extension	0x00	N/A	Binary data extracted from Base64 encoded XML
EncryptedExtension	0x01	N/A	Encrypted binary data extracted from Base64 encoded XML
PropertyBag	0x02	N/A	See PropertyBag canonicalization
Logotype	0x03	MimeType	Binary image data extracted from Base64 encoded XML

Remarks
N/A = zero-length array.
Note the handling of the EncryptedExtension: ExtensionData which is encrypted as described in Encrypted Data must be MACed in encrypted form and then decrypted by the SKS before storing.
A compliant SKS must not allow a given key to be associated with multiple extensions of the same Type.
Type URIs do not have to be recognized by the SKS, since they are intended for interpretation by external applications.
Although not a part of the current SKS specification, an extension could be created for consumption by the SKS only, like downloaded JavaCard code. In that case the associated extension Type URI must be featured in the SKS supported algorithm list. See getDeviceInfo and getExtension.
Qualifier objects must not exceed 128 bytes.

Continued on the next page...
The simplified XML schema extract below describes the KeyGen2 representation of PropertyBag objects:

PropertyBag XML Schema
<xs:element name="PropertyBag"> / <xs:complexType> / <xs:sequence> / <xs:element name="Property" maxOccurs="unbounded"> / <xs:complexType> / <!-- The unique name of the property --> / <xs:attribute name="Name" use="required"/> / <xs:simpleType> / <xs:restriction base="xs:string"> / <xs:minLength value="1"/> / <xs:maxLength value="100"/> / </xs:restriction> / </xs:simpleType> / </xs:attribute> / <!-- The value of the property --> / <xs:attribute name="Value" type="xs:string" use="required"/> / <!-- By default values are read-only but they may be declared as read/writable as well --> / <xs:attribute name="Writable" type="xs:boolean" use="optional"/> / </xs:complexType> / </xs:element> / </xs:sequence> / <!-- Extension type --> / <xs:attribute name="Type" type="xs:anyURI" use="required"/> / <!-- MAC (Message Authentication Code) --> / <xs:attribute name="MAC" type="xs:base64Binary" use="required"/> / </xs:complexType> / </xs:element>

A PropertyBag must be converted to a binary blob before storage in SKS and MACing according to the following:
Each Property is translated into a composite object consisting of the following attributes and transformed representation:

Name	Writable	Value
byte⁮[ ]	bool	byte⁮[ ]

See Data Types
- The resulting Property objects are concatenated in the order they occur in the PropertyBag
Note that there are no delimiters added between attributes or objects. The assembled blob holds the actual ExtensionData.
Enforcement of Property name uniqueness may be delegated to the middleware layer. Also see setProperty.

Continued on the next page...
Below is a KeyGen2 fragment showing an Extension object holding a Base64 encoded Information Card:
<ProvisioningFinalizationRequest ClientSessionID="_126992b6 … a8a6b484db8f" ID="_0fa47ab3c00c … a67992b6ac61c" MAC="GcaqnRxW ... 8kabXDgWr=" Nonce="aqnPb6x0 ... kms34gfW2=" … > / <CertficatePath ID="Key.1" MAC="ngSgmRuPE ... HlFWrM421wY="> <ds:X509Data> <ds:X509Certificate>MIIC2TCCAcGgAwIBAgS … NRT+VokJJsBecyALgeT0Dw==</ds:X509Certificate> </ds:X509Data> <Extension Type="http://schemas.xmlsoap.org/ws/2005/05/identity" / MAC="UMRljeXFd … CrcqcGkI1=">IiBlbmHVy85cZS ... B4bWxuczd3dy53My5vc</Extension> / </CertficatePath> / </ProvisioningFinalizationRequest>

For details on how to map keys and sessions, see setCertificatePath.
In the Information Card sample the primary authentication key (for authenticating to the IDP), would preferable be the PKI key associated by CertificatePath. That is, the issuance of a managed Information Card and its primary key can be fully synchronized making both usage and middleware design straightforward.

The following is a KeyGen2 sample showing the PropertyBag and Logotype objects added to a symmetric key for usage by a HOTP application:
<ProvisioningFinalizationRequest ClientSessionID="_126992b6 … a8a6b484db8f" ID="_0fa47ab3c00c … a67992b6ac61c" MAC="GcaqnRxW ... 8kabXDgWr=" Nonce="aqnPb6x0 ... kms34gfW2=" … > / <CertficatePath ID="Key.1" MAC="ngSgmRuPE ... HlFWrM421wY="> <ds:X509Data> <ds:X509Certificate>MIIC2TCCAcGgAwIBAgS … NRT+VokJJsBecyALgeT0Dw==</ds:X509Certificate> </ds:X509Data> <SymmetricKey MAC="je7KiznTll … vInu7rcqcGkI=">vInt09Esmg94v … YU3tgIdhcNNby</SymmetricKey> <PropertyBag Type="http://xmlns.webpki.org/keygen2/1.0#provider.ietf-hotp" / MAC="jIOHDgwI4dO7Kzs … uEH8MtykIS46JfiJ3N="> / <Property Name="Counter" Value="0" Writable="true"/> / <Property Name="Digits" Value="8"/> / </PropertyBag> / <Logotype MimeType="image/png" / Type="http://xmlns.webpki.org/keygen2/1.0#logotype.application" / MAC="+crSq5fvfx+f … ZmRnhxlj0d=">iAAABKCAIAAACD … tm/AAALjUlEQVRA=</Logotype> </CertficatePath> / </ProvisioningFinalizationRequest>

A HOTP application would preferably also make the corresponding KeyInitializationRequest operation include an endorsement algorithm definition.
## restorePrivateKey (14)
Input
Name	Type	Comment
KeyHandle	int	Local handle to a key belonging to an open provisioning session
PrivateKey	byte⁮[ ]	Private key in PKCS #8 format wrapped as described in Encrypted Data
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values

restorePrivateKey replaces a generated private key with a key supplied by the issuer.
The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = End-Entity Certificate || PrivateKey
Note that PrivateKey objects must be MACed in encrypted form and then decrypted by the SKS before storing.
The purpose of restorePrivateKey (preceded by setCertificatePath), is to install a certificate and private key that the issuer has kept a backup of although the certificate may have been renewed (while using the same key). It may also be used to deploy an entirely issuer-generated credential.

The following KeyGen2 fragment shows how credentials that are to be restored should be formatted:
<ProvisioningFinalizationRequest ClientSessionID="_126992b6 … a8a6b484db8f" ID="_0fa47ab3c00c … a67992b6ac61c" MAC="GcaqnRxW ... 8kabXDgWr=" Nonce="aqnPb6x0 ... kms34gfW2=" … > / <CertficatePath ID="Key.1" MAC="ngSgmRuPE ... HlFWrM421wY="> <ds:X509Data> <ds:X509Certificate>MIIC2TCCAcGgAwIBAgS … NRT+VokJJsBecyALgeT0Dw==</ds:X509Certificate> </ds:X509Data> <PrivateKey MAC="umZCjxSl1zX … CrcqcGkIv4Ki=">cVyZSIiBlbmH ... uczpkcB4bWx3dy53</PrivateKey> / </CertficatePath> / </ProvisioningFinalizationRequest>

For details on how to map keys and sessions, see setCertificatePath.
## pp_deleteKey (50)
Input
Name	Type	Comment
ProvisioningHandle	int	Local handle to an open provisioning session
TargetKeyHandle	int	Local handle to the target key	See Target Key Reference
Authorization	byte⁮[ ]	Key management authorization signature
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values

pp_deleteKey deletes a key created in an earlier provisioning session.
The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = Authorization

A conforming SKS must abort the provisioning session if pp_deleteKey is mixed with other post provisioning operations referring to the same TargetKeyHandle.
Note that the execution of this method must be deferred to closeProvisioningSession.
Regarding delete of PIN and PUK policy objects, see Key Protection Objects.

Continued on the next page...
The following fragment shows how pp_deleteKey operations have been integrated in the KeyGen2 protocol:
<ProvisioningFinalizationRequest ClientSessionID="_126992b6 … a8a6b484db8f" ID="_0fa47ab3c00c … a67992b6ac61c" MAC="GcaqnRxW ... 8kabXDgWr=" Nonce="aqnPb6x0 ... kms34gfW2=" … > / <CertficatePath … > </CertficatePath> / <DeleteKey CertificateFingerprint="mNWEOLlAZrG ... dUg2aLA=" ClientSessionID="_1292389cba4 ... 173d4334" ServerSessionID="_1292389cb8 ... c2ea36e" Authorization="ChPQRDT ... n/dJKrW3L" MAC="AvDWx6xbg3GDGzdz … yJk8Js0Oul+Ba/Xc8="/> / </ProvisioningFinalizationRequest>

Before invoking pp_deleteKey the provisioning middleware needs to perform a number of steps:
1. Find the the old provisioning session associated with the ClientSessionID and ServerSessionID attributes of the DeleteKey element by calling enumerateProvisioningSessions.
2. Find possible keys by calling enumerateKeys and ignoring all but those belonging to the provisioning session found in step #1.
3. For the set of keys found in step #2 call getKeyAttributes while looking for a key having an End-Entity Certificate matching the SHA256 CertificateFingerprint.
4. If step #3 is successful TargetKeyHandle is recovered and pp_deleteKey can be invoked.
If any of these steps fail the provisioning session must be aborted. Also see Remote Key Lookup.
## pp_unlockKey (51)
Input
Name	Type	Comment
ProvisioningHandle	int	Local handle to an open provisioning session
TargetKeyHandle	int	Local handle to the target key	See Target Key Reference
Authorization	byte⁮[ ]	Key management authorization signature
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values

pp_unlockKey works like unlockKey except that authorization is derived from a Target Key Reference instead of a PUK.
The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = Authorization

Note that the execution of this method must be deferred to closeProvisioningSession and that it must (internally) be performed in advance of any pp_updateKey or pp_cloneKeyProtection calls referring to the same TargetKeyHandle.
If the target key is associated with a PUK object the PUK error count must be cleared as well.

The following fragment shows how pp_unlockKey operations have been integrated in the KeyGen2 protocol:
<ProvisioningFinalizationRequest ClientSessionID="_126992b6 … a8a6b484db8f" ID="_0fa47ab3c00c … a67992b6ac61c" MAC="GcaqnRxW ... 8kabXDgWr=" Nonce="aqnPb6x0 ... kms34gfW2=" … > / <CertficatePath … > </CertficatePath> / <UnlockKey CertificateFingerprint="mNWEOLlAZrG ... dUg2aLA=" ClientSessionID="_1292389cba4 ... 173d4334" ServerSessionID="_1292389cb8 ... c2ea36e" Authorization="ChPQRDT ... n/dJKrW3L" MAC="AvDWx6xbg3GDGzdz … yJk8Js0Oul+Ba/Xc8="/> / </ProvisioningFinalizationRequest>

Before invoking pp_unlockKey the provisioning middleware needs to perform the same steps as for pp_deleteKey.
## pp_updateKey (52)
Input
Name	Type	Comment
KeyHandle	int	Local handle to a new key belonging to an open provisioning session
TargetKeyHandle	int	Local handle to the target key	See Target Key Reference
Authorization	byte⁮[ ]	Key management authorization signature
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values

pp_updateKey updates (replaces) a key created in an earlier provisioning session.
The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = End-Entity Certificate || Authorization

The new key must have been fitted with a certificate before this method is called. In addition, the new key must not be PIN‑protected since it supposed to inherit the old key's PIN protection scheme (if there is one).
The target key and and the new key must have identical Key Application Usage.
Note that updating a key involves all related data (see Key Entries), with PIN protection as the only exception.
The KeyHandle of the updated key must after a successful update be set equal to TargetKeyHandle.
A conforming SKS must allow a (single) pp_updateKey combined with an arbitrary number of pp_cloneKeyProtection calls referring to the same TargetKeyHandle.
Note that the execution of this method must be deferred to closeProvisioningSession.

The following fragment shows how pp_updateKey has been integrated in the KeyGen2 protocol:
<ProvisioningFinalizationRequest ClientSessionID="_126992b6 … a8a6b484db8f" ID="_0fa47ab3c00c … a67992b6ac61c" MAC="GcaqnRxW ... 8kabXDgWr=" Nonce="aqnPb6x0 ... kms34gfW2=" … > / <CertficatePath ID="Key.1" MAC="ngSgmRuPE ... HlFWrM421wY="> <ds:X509Data> <ds:X509Certificate>MIIC2TCCAcGgAwIBAgS … NRT+VokJJsBecyALgeT0Dw==</ds:X509Certificate> </ds:X509Data> <UpdateKey CertificateFingerprint="mNWEOLlAZrG ... dUg2aLA=" ClientSessionID="_1292389cba4 ... 173d4334" ServerSessionID="_1292389cb8 ... c2ea36e" Authorization="ChPQRDT ... n/dJKrW3L" MAC="AvDWx6xbg3GDGzdz … yJk8Js0Oul+Ba/Xc8="/> / </CertficatePath> / </ProvisioningFinalizationRequest>

Before invoking pp_updateKey the provisioning middleware needs to perform the same steps as for pp_deleteKey.
KeyHandle is the handle associated with CertficatePath.
## pp_cloneKeyProtection (53)
Input
Name	Type	Comment
KeyHandle	int	Local handle to a new key belonging to an open provisioning session
TargetKeyHandle	int	Local handle to the target key	See Target Key Reference
Authorization	byte⁮[ ]	Key management authorization signature
MAC	byte⁮[32]	Vouches for the integrity and authenticity of the operation

Output
Name	Type	Comment
Status	byte	See Return Values

pp_cloneKeyProtection clones the protection scheme of a key created in an earlier provisioning session and applies it to a newly created key.
The MAC uses the method described in MAC Operations where Data is arranged as follows:
Data = End-Entity Certificate || Authorization

The new key must have been fitted with a certificate before this method is called. In addition, the new key must not be PIN‑protected since it supposed to inherit the old key's PIN protection scheme (if there is one). Inheritance does not mean “copying” but linking the new key to an existing PIN object. See Key Protection Objects.
The target key and and the new key must have identical Key Application Usage.
Note that an SKS must not allow inheritance of PIN protection schemes except device PIN (see createKeyPair) or a custom PIN protection scheme with grouping <> none (see PIN Grouping).
A conforming SKS must allow multiple pp_cloneKeyProtection calls referring to the same TargetKeyHandle.
Note that the execution of this method must be deferred to closeProvisioningSession.

The following fragment shows how pp_cloneKeyProtection has been integrated in the KeyGen2 protocol:
<ProvisioningFinalizationRequest ClientSessionID="_126992b6 … a8a6b484db8f" ID="_0fa47ab3c00c … a67992b6ac61c" MAC="GcaqnRxW ... 8kabXDgWr=" Nonce="aqnPb6x0 ... kms34gfW2=" … > / <CertficatePath ID="Key.1" MAC="ngSgmRuPE ... HlFWrM421wY="> <ds:X509Data> <ds:X509Certificate>MIIC2TCCAcGgAwIBAgS … NRT+VokJJsBecyALgeT0Dw==</ds:X509Certificate> </ds:X509Data> <CloneKeyProtection CertificateFingerprint="mNWEOLlAZrG ... dUg2aLA=" ClientSessionID="_1292389cba4 ... 173d4334" ServerSessionID="_1292389cb8 ... c2ea36e" Authorization="ChPQRDT ... n/dJKrW3L" MAC="AvDWx6xbg3GDGzdz … yJk8Js0Oul+Ba/Xc8="/> / </CertficatePath> / </ProvisioningFinalizationRequest>

Before invoking pp_cloneKeyProtection the provisioning middleware needs to perform the same steps as for pp_deleteKey.
KeyHandle is the handle associated with CertficatePath.
## enumerateKeys (70)
Input
Name	Type	Comment
KeyHandle	int	Input enumeration handle

Output
Name	Type	Comment
Status	byte	See Return Values
KeyHandle	int	Output enumeration handle
The following element must only be emitted if KeyHandle <> 0xFFFFFFFF
ProvisioningHandle	int	Handle to the associated provisioning session object

enumerateKeys enumerate keys for closed provisioning sessions. Closed provisioning session means that the key is ready for usage by applications.
The input KeyHandle is initially set to 0xFFFFFFFF to start an enumeration round.
Succeeding calls should use the output KeyHandle as input to the next call.
When enumerateKeys returns with a KeyHandle = 0xFFFFFFFF there are no more key objects to read.
## getKeyAttributes (71)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key

Output
Name	Type	Comment
Status	byte	See Return Values
IsSymmetricKey	bool	True if the active key is symmetric. See setSymmetricKey
AppUsage	byte	See createKeyPair
FriendlyName	byte⁮[ ]
PathLength	byte	‪‫‬‭‪‏‪‏‎See setCertificatePath
X509Certificate...	byte⁮[ ]
EndorsedAlgorithms	byte	‎See createKeyPair
EndorsedAlgorithm...	uri
Extensions	short	Number of Type URIs	See addExtension
Type...	uri	Extension Type URI. Repeated object

getKeyAttributes returns attribute data for provisioned keys.
For asymmetric keys the public key of the End-Entity Certificate signifies RSA or ECC.
## getKeyProtectionInfo (72)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key

Output
Name	Type	Comment
Status	byte	See Return Values
ProtectionStatus	byte	See ProtectionStatus
PUKFormat	byte	Copy of Format defined by createPUKPolicy [1]
PUKRetryLimit	short	Copy of RetryLimit defined by createPUKPolicy [1]
PUKErrorCount	short	Current PUK error count for keys protected by a local PUK policy object [1]
UserDefined	bool	Exact copies of the corresponding createPINPolicy parameters for keys protected by a local PIN policy object [1]
UserModifiable	bool
Format	byte
RetryLimit	short
Grouping	byte
PatternRestrictions	byte
MinLength	short
MaxLength	short
InputMethod	byte
PINErrorCount	short	Current PIN error count for keys protected by a local PIN policy object [1]
BiometricProtection	byte	Exact copies of the corresponding createKeyPair parameters [2]
PrivateKeyBackup	bool
ExportProtection	byte
DeleteProtection	byte
EnablePINCaching	bool

getKeyProtectionInfo returns information about the protection scheme for a key including possible biometric options. In addition, the call retrieves the current protection status for the key.
Note 1: Fields must be set to zero if they do not apply to the key in question.
Note 2: PrivateKeyBackup must also be set if the private key has been supplied through restorePrivateKey.

Continued on the next page...

The following table illustrates how the ProtectionStatus bit field should be interpreted:
Bit	Comment
0	The key is protected by a local PIN policy object
1	The key is protected by a local PUK policy object. This bit must be combined with bit 0
2	The key has locked-up due to PIN errors. This bit must be combined with bit 0
3	The key has locked-up due to PUK errors. This bit must be combined with bit 1
4	The key is protected by a device PIN. Information about device PINs is out of scope for the SKS API. This bit must be the only active bit if applicable

If all bits are zero the key is not PIN protected.
## getExtension (73)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Type	uri	Type URI. See addExtension

Output
Name	Type	Comment
Status	byte	See Return Values
SubType	byte	Exact copies of the corresponding addExtension parameters
Qualifier	byte⁮[ ]
ExtensionData	blob

getExtension returns a typed extension object associated with a key.
Note that encrypted extensions are decrypted during provisioning.
If the extension is intended to be consumed by the SKS, ExtensionData must be returned as a zero-length array.
## setProperty (74)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Type	uri	Type URI which must identify a PropertyBag extension. See addExtension
Name	byte⁮[ ]	Property name
Value	byte⁮[ ]	Property value

Output
Name	Type	Comment
Status	byte	See Return Values

setProperty sets a Property in a PropertyBag linked to a key.
If the named Property does not exist or is not writable, an error must be returned.
## deleteKey (80)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Authorization	byte⁮[ ]	Zero-length array, PIN, or PUK depending on Key Delete

Output
Name	Type	Comment
Status	byte	See Return Values

deleteKey removes a key from the Credential Database.
If the key is the last belonging to a provisioning session, the session data objects are removed as well.
Invalid Authorization data to the key must return ERROR_AUTHORIZATION status.
A conforming SKS may introduce physical presence methods like GPIO-based buttons, circumventing key delete policy settings.
Regarding delete of PIN and PUK policy objects, see Key Protection Objects.
## exportKey (81)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Authorization	byte⁮[ ]	Zero-length array, PIN, or PUK depending on Key Export

Output
Name	Type	Comment
Status	byte	See Return Values
Key	byte⁮[ ]	Unencrypted key. For type information see getKeyAttributes

exportKey exports a private or secret key from the Credential Database.
Invalid Authorization data to the key must return ERROR_AUTHORIZATION status.
Private (asymmetric) keys must be exported in PKCS #8 format.
If a non-exportable key is referred to, exportKey must return ERROR_NOT_ALLOWED status.
## unlockKey (82)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Authorization	byte⁮[ ]	PUK

Output
Name	Type	Comment
Status	byte	See Return Values

unlockKey re-enables a key that has been locked due to erroneous PIN entries.
Note that this method only applies to keys that are protected by local PIN and PUK policy objects.
Invalid Authorization data (PUK) to the key must return ERROR_AUTHORIZATION status.
If unlockKey succeeds all keys sharing the PIN object will be unlocked. See PIN Grouping.
## changePIN (83)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Authorization	byte⁮[ ]	Original PIN
NewPIN	byte⁮[ ]	The requested new PIN

Output
Name	Type	Comment
Status	byte	See Return Values

changePIN modifies a PIN for a key.
Note that the key must be protected by a local PIN policy object having the UserModifiable attribute set.
Invalid Authorization data (PIN) to the key must return ERROR_AUTHORIZATION status.
If changePIN succeeds all keys sharing the PIN object will be updated. See PIN Grouping.
## setPIN (84)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Authorization	byte⁮[ ]	PUK string
NewPIN	byte⁮[ ]	The requested new PIN

Output
Name	Type	Comment
Status	byte	See Return Values

setPIN sets a PIN for a key regardless of PIN block status since it uses a PUK as authorization.
Note that the key must be protected by local PUK and PIN policy objects where the latter have the UserModifiable attribute set.
Invalid Authorization data (PUK) must return ERROR_AUTHORIZATION status.
If setPIN succeeds all keys sharing the PIN object will be updated and unlocked. See PIN Grouping.
## signHashedData (100)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Algorithm	uri	Signature algorithm URI. See Asymmetric Key Signatures ‎
Parameters	byte⁮[ ]	Parameters needed by some signature algorithms
Authorization	byte⁮[ ]	Holds a PIN or is of zero length if no PIN is supplied
Data	byte⁮[ ]	Hashed data to be signed. Also see CryptoDataSize

Output
Name	Type	Comment
Status	byte	See Return Values
Result	byte⁮[ ]	Signed data including algorithm-specific padding

signHashedData performs an asymmetric key signature operation on the input Data object.
Data must be hashed as required by the signature algorithm.
The Parameters object must be of zero length for signature algorithms not needing additional input.
Invalid Authorization data (PIN) to the key must return ERROR_AUTHORIZATION status.
The length of Data must match the hash algorithm. Note that signature algorithms that do not specify a hash algorithm impose no tests on Data length. For RSA signatures without hash algorithm the signature packet must be formatted according to PKCS #1 but without hash algorithm identifiers:
EMSA = 0x00 || 0x01 || PS || 0x00 || Data
## asymmetricKeyDecrypt (101)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Algorithm	uri	Encryption algorithm URI. See Asymmetric Key Encryption ‎
Parameters	byte⁮[ ]	Parameters needed by some encryption algorithms
Authorization	byte⁮[ ]	Holds a PIN or is of zero length if no PIN is supplied
Data	byte⁮[ ]	Encrypted data

Output
Name	Type	Comment
Status	byte	See Return Values
Result	byte⁮[ ]	Decrypted data

asymmetricKeyDecrypt performs an asymmetric key decryption operation on the input Data object.
Data must be padded as required by the encryption algorithm like PKCS #1 for http://www.w3.org/2001/04/xmlenc#rsa-1_5.
The Parameters object must be of zero length for encryption algorithms not needing additional input.
Invalid Authorization data (PIN) to the key must return ERROR_AUTHORIZATION status.

## keyAgreement (102)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Algorithm	uri	Key agreement algorithm URI. See Diffie-Hellman Key Agreement ‎
Parameters	byte⁮[ ]	Parameters needed by some key agreement algorithms
Authorization	byte⁮[ ]	Holds a PIN or is of zero length if no PIN is supplied
PublicKey	byte⁮[ ]	The other party's public key

Output
Name	Type	Comment
Status	byte	See Return Values
Key	byte⁮[ ]	Shared secret key

keyAgreement performs an asymmetric key agreement operation resulting in a shared secret key.
The Parameters object must be of zero length for key agreement algorithms not needing additional input.
Invalid Authorization data (PIN) to the key must return ERROR_AUTHORIZATION status.

## performHMAC (103)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Algorithm	uri	HMAC algorithm URI. See HMAC Operations ‎
Authorization	byte⁮[ ]	Holds a PIN or is of zero length if no PIN is supplied
Data	blob	Data to be HMACed. Also see CryptoDataSize

Output
Name	Type	Comment
Status	byte	See Return Values
Result	byte⁮[ ]	HMACed data

performHMAC performs a symmetric key HMAC operation on the input Data object.
Invalid Authorization data (PIN) to the key must return ERROR_AUTHORIZATION status.
## symmetricKeyEncrypt (104)
Input
Name	Type	Comment
KeyHandle	int	Local handle to the target key
Algorithm	uri	Encryption algorithm URI. See Symmetric Key Encryption ‎
Mode	bool	True for encryption, false for decryption
IV	byte⁮[ ]	Initialization Vector. Zero length for the XML Encryption algorithms
Authorization	byte⁮[ ]	Holds a PIN or is of zero length if no PIN is supplied
Data	blob	Data to be encrypted or decrypted. Also see CryptoDataSize

Output
Name	Type	Comment
Status	byte	See Return Values
Result	blob	Encrypted or decrypted data

symmetricKeyEncrypt performs a symmetric key encryption or decryption operation on the input Data object.
Note that if an IV (Initialization Vector) is not required by the encryption algorithm, IV must be of zero length.
Invalid Authorization data (PIN) to the key must return ERROR_AUTHORIZATION status.

# Session Security Mechanisms
After the SessionKey has been created the actual provisioning methods can be called. Depending on the specific method downloaded data may be confidential or need to be authenticated. For certain operations the SKS needs to prove for the issuer that sent data indeed stems from internal SKS operations which is referred to as attestations.
This section describes the security mechanisms used during a provisioning session. Also see SessionKeyLimit.
String literals like "Encryption Key" featured in the following definitions must be supplied “as is” without length indicators, while when being a part of MAC or attestation Data arguments must be treated as described in Data Types.

## Encrypted Data
During provisioning encrypted data is occasionally exchanged between the issuer and the SKS. The encryption key is created by the following key derivation scheme:
EncryptionKey = HMAC-SHA256 (SessionKey, "Encryption Key")
EncryptionKey must only be used with the AES256-CBC algorithm. Note that the IV (Initialization Vector) must always be prepended to the encrypted data as in XML Encryption.

## MAC Operations
In order to verify the integrity of provisioned data, many of the provisioning methods mandate that the data-carrying arguments are included in a MAC (Message Authentication Code) operation as well. MAC operations use the following scheme:
MAC = HMAC-SHA256 (SessionKey || MethodName || MACSequenceCounter, Data)
MethodName is the string literal of the target method like "closeProvisioningSession", while Data represents the arguments as specified for the actual method. Note that individual elements featured in Data must use the representation described in Data Types.
After each MAC operation, MACSequenceCounter must be incremented by one. Due the use of a sequence counter, the provisioning system must honor the order of objects as defined by the issuer.

## Attestations
Attestations created by the SKS are identical to MAC Operations where MethodName is set to "Device Attestation".

## Target Key Reference
In order to perform post provisioning operations the issuer must provide evidence of ownership to keys. Target Key Reference denotes a key management authorization signature scheme using the KeyManagementKey associated with the “owning” provisioning object of the target key (see Provisioning Objects) according to the following:
Authorization = Sign (HMAC-SHA256 (SessionKey || Device Certificate, End-Entity Certificate))
Notes:
- All elements must be represented “as is” in the HMAC operation, excluding length information
- Sign must use an PKCS #1 RSASSA signature for RSA keys and ECDSA for ECC keys with the private key associated with KeyManagementKey, and utilizing SHA256 as hash function
- An SKS must verify that the signature validates with respect to the public key (KeyManagementKey) as well as checking that End-Entity Certificate matches TargetKeyHandle
- If a KeyManagementKey is not present in the target key's provisioning object, the key is considered “not updatable” and the provisioning session must be aborted
# Sample Session
The following provisioning sample session shows the sequence for creating an X.509 certificate with a matching PIN and PUK protected private key:
ProvisioningHandle, ... = createProvisioningSession (…)
PUKPolicyHandle = createPUKPolicy (ProvisioningHandle, ...)
PINPolicyHandle = createPINPolicy (ProvisioningHandle, , PUKPolicyHandle, ...)
KeyHandle, ... = createKeyPair (ProvisioningHandle, , PINPolicyHandle, …)
External certification of the generated public key happens here...
setCertificatePath (KeyHandle, ...)
closeProvisioningSession (ProvisioningHandle, ...)

Note that Handle variables are only used by local middleware, while (not shown) variables like SessionKey, MAC, ID, etc. are primarily used in the communication between an issuer and the SKS.
If keys are to be created entirely locally, this requires local software emulation of an issuer.

# Reference Implementation
To further guide implementers, an open source SKS reference implementation in java® is available including a JUnit suite.
URL: http://code.google.com/p/openkeystore

# Remote Key Lookup
In order to update keys and related data, SKS supports post provisioning operations like pp_deleteKey where issuers are securely shielded from each other by the use of a KeyManagementKey.
However, depending on the use-case, an issuer may need to get a list of applicable keys, before launching post provisioning operations. Such a facility is available in KeyGen2 as illustrated by the XML fragment below:
<CredentialDiscoveryRequest … > / <LookupSpecifier ID="Lookup.1" Nonce="nSgmg4cznqE ... WrH2421w9SYA="> <SearchFilter Email="john.doe@example.com"/> <ds:Signature> <ds:SignedInfo> <ds:CanonicalizationMethod Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/> <ds:SignatureMethod Algorithm="http://www.w3.org/2001/04/xmldsig-more#rsa-sha256"/> <ds:Reference URI="#Lookup.1"> <ds:Transforms> <ds:Transform Algorithm="http://www.w3.org/2000/09/xmldsig#enveloped-signature"/> <ds:Transform Algorithm="http://www.w3.org/2001/10/xml-exc-c14n#"/> </ds:Transforms> <ds:DigestMethod Algorithm="http://www.w3.org/2001/04/xmlenc#sha256"/> <ds:DigestValue>JBfoi8iBKRyWxXYlTTU1cdyybMTyJr+WDW+qCJdxoGE=</ds:DigestValue> </ds:Reference> </ds:SignedInfo> <ds:SignatureValue>mSMaH6wChPQRDT... JKrW3n/dL7seGbg==</ds:SignatureValue> <ds:KeyInfo> <ds:RSAKeyValue> <ds:Modulus>ALhBpUjJK/mSjPAe/ … fXG8z1V3mVDZTBM7eZ</ds:Modulus> <ds:Exponent>AQAB</ds:Exponent> </ds:RSAKeyValue> / </ds:KeyInfo> </ds:Signature> </LookupSpecifier> / </CredentialDiscoveryRequest>

The example works as follows:
1. Verify that the Signature is technically valid. Note that the actual issuer is ignored since an SKS has no opinion about what issuers are trustworthy or not.
2. Verify that the freshness Nonce matches SHA256 (ClientSessionID || ServerSessionID).
   See createProvisioningSession and Data Types.
3. Enumerate all sessions having a KeyManagementKey matching the public key of the Signature. This serves as an Issuer Filter. See enumerateProvisioningSessions.
4. From step #3 enumerate all matching SKS keys and related certificates. See enumerateKeys and getKeyAttributes.
5. Collect the keys from step #4 that also feature the e-mail addresss "john.doe@example.com" in the
   End-Entity Certificate.

The result is sent back to the issuer in the form of a list of SHA256 (End-Entity Certificate) fingerprints and session IDs.
Remote key lookups are performed at the middleware level since they are passive, XML intensive, and do not access private or secret keys. The primary purpose with credential lookups is improving provisioning robustness, while the Issuer Filter protects user privacy by constraining lookup data to the party to where it belongs.
# Security Considerations
This document does not cover the security of the actual key-store since SKS does not differ from other systems like smart cards in this respect.
However, SKS introduces a concept sometimes referred to as “air-tight” provisioning which has some specific security characteristics. One of the most critical operations in SKS is the creation of a shared SessionKey because if such a key is intercepted or guessed by an attacker, the integrity of the entire session is potentially jeopardized.
If you take a peek at createProvisioningSession you will note that the SessionKey depends on issuer-generated and SKS-generated ephemeral public keys. It is pretty obvious that malicious middleware could replace such a key with one it has the private key to and the issuer wouldn't notice the difference. This is where the attestation signature comes in because it is computationally infeasible creating a matching signature since the both of the ephemeral public keys are enclosed as a part of the signed attestation object. That is, the issuer can when receiving the response to the provisioning session request, easily detect if it has been manipulated and cease the rest of the operation.
As earlier noted, the randomness of the SessionKey is crucial for all provisioning operations.
Missing or repeated objects are indirectly monitored by the use of MACSequenceCounter, while the SKS “book-keeping” functions will detect other possible irregularities during closeProvisioningSession. This means that an issuer should not consider issued credentials as valid unless it has received a successful response from closeProvisioningSession.
The SessionKeyLimit attribute defined in createProvisioningSession is another security measure which aims to limit exhaustive attacks on the SessionKey.
For algorithms that are considered as vulnerable to brute-force key searches, a simple workaround is adding a short initial delay to the applicable User API method. Since SKS is exclusively intended for user authentication a 1-100 ms delay imposes a (from the user's point of view), hardly noticeable impact on the performance.
By using the EndorsedAlgorithm option, issuers can specify exactly which algorithms that are permitted for a given key.
One of the most significant features of SKS is the fact that it is identified by a digital certificate, preferably issued by a known vendor of trusted hardware. This enables the issuer to securely identify the key-container both from a cryptographic point of view (brand, type etc) and as a specific unit. The latter makes it possible to communicate the container identity as an SHA1 fingerprint of the Device Certificate which facilitates novel and secure enrollment procedures, typically eliminating the traditional sign-up password.
That any issuer (after the user's consent), can provision keys may appear a bit scary but keys do not constitute of executable code making it less interesting in tricking users accepting “bad” issuers. In addition, the provisioning middleware is also able to validate incoming data for “sanity” and even abort unreasonable requests, such as asking for 10 keys or more to be created.
Although not a part of SKS, KeyGen2 puts a signature derived from the SessionKey over the provisioning session response. The latter holds an HTTPS ServerCertificateFingerprint giving the issuer an opportunity verifying that there actually is a “straight line” between the client and server.
One might suspect that the VSD scheme by relying on a static, potentially issuance-wide KeyManagementKey could introduce client-side vulnerabilities but that is unlikely to be the case: If a key management signature is intercepted by an attacker, the inclusion of a high entropy SessionKey and the Device Certificate renders it useless in another session or device. It is also worth noting that the post provisioning operations by design do not expose secret or private key data.
There is no protection against DoS (Denial of Service) attacks on SKS storage space due to malicious middleware.
SKS does not have any built-in notion of policy, it is up to the individual issuer deciding about suitable key protections options, key sizes, and private key backups.

# Intellectual Property Rights
This document contains several constructs that could be patentable but the author has no such interests and therefore puts the entire design in public domain allowing anybody to use all or parts of it at their discretion. In case you adopt something you found useful in this specification, feel free mentioning where you got it from 
Note: it is possible that there are pieces that already are patented by other parties but the author is currently unaware of any IPR encumbrances.
Some of the core concepts have been submitted to http://defensivepublications.org and subsequently been published in IP.COM's prior art database.
# References

KeyGen2	TBD
PKCS #1	TDB
PKCS #8	TBD
ECDSA	TBD
AES256-CBC	TBD
HMAC-SHA1	TBD
HMAC-SHA256	TBD
X.509	TBD
SHA256	TBD
TPM 1.2	TBD
Diffie-Hellman	TBD
S/MIME	TBD
UTF-8	TBD
XML Encryption	TBD
XML Signature	TBD
FIPS 197	TBD
FIPS 186-3	TBD
Information Card	TBD
Base64	TBD
HOTP	TBD
JavaCard	TBD
JCE	TBD
CryptoAPI	TBD
PKCS #11	TBD
Global Platform	TBD
TLS	TBD
XML Schema	TBD
SP800-56A	TBD
Kerberos	TBD

# Acknowledgments
SKS and KeyGen2 heavily build on schemes pioneered by other individuals and organizations, most notably:
- CT-KIP by RSA Security: KeyGen2 format and basic operation
- ObC by Nokia: Key management through dynamic deployment of issuer-specific symmetric keys (VSD), and support for keys bound to downloaded data (in ObC code)
- SCP80 by GlobalPlatform: Secure messaging including “rolling MACs”
- CertEnroll by Microsoft: Processes
There is also a bunch of individuals that have been instrumental for the creation of SKS. I need to check who would accept to be mentioned :-)
KeyGen2 is an “homage” to Netscape Communications Corp. who created the first on-line provisioning system called KeyGen.

# Author
Anders Rundgren
anders.rundgren@telia.com

# To Do List
Although it would be nice to say “it is 100% ready” there are still a few things missing:
- Firmware upgrade API method
- Investigating possible token “wipe” options
- Minimalistic PINpad support
- Investigating “physical presence” GPIO options
- Language check
- Filling in the references